## Slide 1: MNS Intelligent Solution with M10x
PMT-Automation Solutions, June 2013 1TNC912001N0203
Quick Guide

## Slide 2: Introduction to M10x Content
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project Reference
Product guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions

## Slide 3: Motor Management: Tasks of Motor Management
* Motor failure rate is conservatively estimated as 3-5% per year
In Mining, Pulp and Paper industry, motor failure rate can be as high as 12%.
In the Process Industry there are hundreds of motors. To run a plant efficiently it becomes important to protect and control motors effectively and safely.
Tasks of Motor Management:
  Control the motor (local / remote, start / stop, trip reset etc.)
  Monitor and Report to ensure optimized and continuous operation:
    Online motor Monitoring and protection
    Offline motor management
  Diagnose and Report
    Identify the fault reason
    Clear the fault as fast as possible to restart motor.
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions

## Slide 4: Motor Management: Intelligent Motor Management
Intelligent motor management features are integrated smoothly into switchgear solution.
To minimize life cycle costs, customers invest more money to use intelligent LV switchgear solutions.
Intelligent motor management features such as control, protection, monitor and communication, are integrated smoothly into switchgear solution.
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions
Notes: What is intelligent LV switchgear Solution?
3 solutions available

## Slide 5: Advantages of Intelligent Switchgear: Comparison of technologies
Replace numerous conventional components with one intelligent device
Intelligent Starter
  1 Main isolator
  3 Main fuses
  2 Control fuses
  1+ Contactor
  Current / Voltage transformer
  1 Intelligent Relay
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions
Conventional Starter
  1 Main isolator
  3 Main fuses
  2 Control fuses
  1+ Contactor
  Current / Voltage transformer
  Thermal overload relay
  Earth fault relay
  Thermistor relay
  Ammeter
  Counter (switching, running)
  Pushbuttons and lamps
  Interposing relays
  Marshalling Cabinets

## Slide 6: Advantages of Intelligent Switchgear: Comparison of technologies
  Less components, less wiring for one starter
  Reduced module size
  Standardized module types
  Faster testing and commissioning
Protection, Control, Monitoring, Communication in One Device:
Advanced Monitoring, Diagnosis and Reporting features
  Local operator panel for motor monitoring and diagnosis
  Continuous online/offline data reporting to the network
  Detailed diagnosis information when motor is at fault
  Providing preventative maintenance information
MNS3.0+M10x Starter Vs MNS3.0 Conventional Starter
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions

## Slide 7: Advantages of Intelligent Switchgear: Improving RAMS with MNS3.0+M10x
  Improving Safety
  The solution has been proven and type tested as part of MNS3.0 assembly. Providing an operator panel in front of every starter makes it easy and safe for operation.
  Improving Reliability
  The solution was introduced to the market in 2004 and has large installed base across different industries with a growing global reputation.
  Improving Availability
  Standardized solution requires minimum replacement time.
  Improving Maintainability
  Preventative and maintenance information available to ensure maintenance and service provided in time and as needed.
Reliability, Availability, Maintainability & Safety
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions

## Slide 8: MNS3.0+M10x Solution: Typical Applications
MNS3.0 Withdrawable Modules M10x is mounted inside the MNS drawer. In case of a problem a drawer can be replaced by a spare part without the need of wiring work inside the switchgear.
First M10x+M10x swgr was manufactured in 2004!
Latest updated in 2013!
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions

## Slide 9: MNS3.0+M10x Solution: Typical Applications
MNS3.0 Removable Modules
  M10x is also provided as part of the standard solutions for MNS3.0 mining concept switchgear removable module design. In a removable module, replacing the module may require additional work.
Fixed design
  Such as ACB instrument chambers, customized fixed modules etc..
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions
M10x removable module in new Mining Concept MNS3.0 switchboard!

## Slide 10: MNS3.0+M10x Solution: Test & Certificates
CE Certificate
CCC Certificate
Profibus Certificate
ASTA Certificate
EMC Tested
IEC Tested
Ex e Tested
ABS & ATEX certificate applications are scheduled on 2013!
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions

## Slide 11: Project References A world of experience
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions
With nearly ten years of exposure to the market, our product has large installed base and built a global reputation across M&M, COG, P&P, Water Treatment Plant and Power Plant etc
Sydney Water
SSWA
Goro Nickle
Rio Tinto
Sino Iron
GLNG
QGC
Ichthys
Huatai Paper
APM3
Nui Phao Mine
Waist (Aramco)
etc
Notes: Photo: Better photo should be replaced. Preferably be replaced by new photos from CNILX

## Slide 12: Project References System Integration Experience
M10x device type released in 800xA solution library!
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions
ABB Industrial IT (800xA, AC500)
Siemens/PCS7
Yokogawa/CS1000
Emerson / Delta V
Invensys / Foxboro
Rockwell /Control logix
Allen Bradley
Other smaller PLC systems etc

## Slide 13: Product Guide
Protection, Control and Monitoring in one unit
  Up to 13 DIs and 5DOs in one unit
0.08-63A current measuring in one unit
  Current & Voltage Measuring in one unit
 Easy to setup, easy to operate, easy to use!
M10x device is a ONE size device
Multiple product choices for different applications
Simplified or Advanced Version-M101 or M102
  Fieldbus type- PROFIBUS or Modbus
  Aux Supply and DI type – 24Vdc, 110Vac, 240Vac
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions
Notes: 110x140x75mm
91x75x24.3mm (MD21)
88x50x24.3mm(MD31)

## Slide 14: Product Guide Assortment
One size device M10x with multiple choices,
Simplified or Advanced Version-M101 or M102
  Fieldbus type- PROFIBUS or Modbus
  Aux Supply and DI type – 24Vdc, 110Vac, 240Vac
Operator Panel MDx
MD31 Control & Indication
MD21 (LCD panel) Control, Monitor, Paramerization
Current Transformer
ZCT for Earth Fault Current
External CT for Current range >63A
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions
Notes: Photos: Product photo should have white background and with angle (refer to imagery_page14.pdf as per attached file)

## Slide 15: Product Guide Digital Inputs & Outputs
Digital inputs | M10x (24VDC) | M10x (110V or 230VAC)
Configurable DI | 13 | 9
Relay outputs | M102 | M101
Contactor relay output | 3 NO | 2 NO
Configurable relay output | 1 NO +1 NC 1 NO | 1 NO
Note for configurable DI:
  DC input detection time <=20ms
  AC input detection time <=50ms
Note for DO relay:
  Relay contact max 2A (24VDC DC13 or 230VAC AC15)
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions

## Slide 16: Product Guide: Control Functions
Control functions | M101 | M102
Non Reversing DOL |  | 
Reversing DOL |  | 
Non Reversing DOL with Remote Control Unit |  | 
Reversing DOL with Remote Control Unit |  | 
Non Reversing Star-Delta | - | 
Non Reversing Two Speed | - | 
Actuator | - | 
Autotransformer | - | 
Non Reversing Soft-Starter | - | 
Reversing Soft-Starter | - | 
Contactor Feeder |  | 
Feeder (motor operated MCCB only) |  | 
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions
Notes: Supporting 12 starter control functions

## Slide 17: Product Guide: Protection Functions
Protection functions | M101 | M102
Thermal Overload |  | 
Thermal Overload Eex-e |  | 
Stall Protection |  | 
Phase Failure |  | 
Phase Current Unbalance |  | 
No- Load Protection |  | 
Under- Load Protection |  | 
Earth Fault |  | 
Motor Temperature (PTC) | - | 
Under-Voltage with Auto Restart | - | 
Long Start Protection |  | 
Start Limitation |  | 
Start Interlock |  | 
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions
Notes: 13 types of motor protection functions

## Slide 18: Product Guide: Monitoring & Reporting Functions
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions
Monitoring & Reporting functions | M101 | M102
Motor Status (Run, Stop, Alarm, Trip) |  | 
Phase Current L1,L2,L3 (A) |  | 
Phase Current L1,L2,L3 (%) |  | 
Thermal Capacity (%) |  | 
Time to Trip & Time to Reset |  | 
Power Factor | - | 
Line voltage L1-L2, L1-L3,L2-L3 (V) | - | 
Frequency (Hz) | - | 
Earth Fault Current (A) |  | 
PTC Value (ohm) | - | 
Active Power (kW), Apparent Power (kVA) | - | 
Energy (kWh) | - | 
Actual Starting Time |  | 
Phase (current) unbalance (%) |  | 
Alarm / Trip on protection functions |  | 
Digital Input Status |  | 
* All available via MDx and Fieldbus.

## Slide 19: Product Guide: Maintenance & Service Data
Maintenance & Service Data
  Running time (max value 65534)
  Stopped time (via serial link, max value 65534)
  Switching number(max value 65534)
  Running time and Switching number alarm setting range: 1…65534hrs
  Energy Counter (kWh)
  Number of Trips
  Current before last trip
  SOE up to 256 events
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions
Notes: ________________________________________________________________________________________________________________________________________________________________________________________

## Slide 20
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions
Local Operator Panel MD21/MD31
Real time alarm/trip message, up to 256 events with time stamp(MD21)
Configurable LEDs’ (4sets) color and function ( LED label is replaceable)
Direct Start 1/Start 2/ Stop (Reset) control buttons.
Selectable running parameters to be displayed (max.13pages)
Navigational buttons available for parameter setting on MD21
Time setting, Parameter Loading & Self-testing functions on MD21
IP54 protection design
Product Guide: Operator Panels
Notes: Photos: Product photo should have white background and with angle (refer to imagery_page14.pdf as per attached file)

## Slide 21: Product Guide: Engineering Tool- Parameters Setup Software
MCUSetup Software
Connected to M10x via MDx panel on module front
For connection a special cable is used to connect to MDx
All functions can be parameterized for the different M10x types
Works with Win XP, Win 7 &8
Can be used for live demonstration of parameter setting with Demo box
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions

## Slide 22: Product Guide: Device Selection Guide
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions
Check what protection / control / monitoring function is required as per customer specification  M101 or M102
2. Check the fieldbus communication
 M10x-M for Modbus or M10x-P for PROFIBUS DP
Check control voltage requirement (power supply and DI) to finalize the product type (24VDC, 110VAC or 230VAC)
Select operator panel  MD31 (simple) or MD21 (LCD)
Refer to engineering guideline or coordination table for motor starter type coordination
Define MNS 3.0 module size with M10x (minimum size 8E/4 with MD31 only!)
M101 Or M102?
Modbus or PROFIBUS?
24VDC,110VAC or 230VAC?
Module size?
MD21 or MD31?
Type1 or Type 2?

## Slide 23: Product Guide: Coordination Table
Main Switch | Voltage | KA Rating | Starter Type | Fuse Type | Coordination No.
Switch Fuse | 400V | 50/65/80KA | NS | aM | FM40080NSM10XT2
Switch Fuse | 400V | 50/65/80KA | NS | gG | FG40080NSM10XT2
Switch Fuse | 400V | 100KA | NS | aM | FM40100NSM10XT2
Switch Fuse | 400V | 100kA | NS | gG | FG40100NSM10XT2
Switch Fuse | 400V | 50/65/80KA | HD | aM | FM40080HDM10XT2
Switch Fuse | 400V | 50/65/80KA | HD | gG | FM40080HDM10XT2
............ |  |  |  |  | 
Switch Fuse | 690V | 80KA | NS | gG | FG69080NSM10XT2
Switch Fuse | 690V | 80KA | HD | aM | FM69080HDM10XT2
Switch Fuse | 690V | 80KA | HD | gG | FG69080HDM10XT2
“ M10x Coordination Table Rev2” is available in product support database and is in line with ABB group SOC table on the intranet
(http://applications.it.abb.com/SOC/Page/Selection.aspx)
Selected MNS3.0 +M10x modules are verified tested (ASTA certificate is available in MNS support database)
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions
Notes: Note 1: Recommend to use the table format as attached (Table.pdf)

## Slide 24: Serial Communication: PROFIBUS DP Communication
M10x-P No.1 M10x-P No. 2 M10x-P No. 3 …………. M10x-P No. 31
Max 31 M10x-P devices per segment, max 1.5M.
Multiple segments possible, repeater & bus termination needed
Typ. command execution time for one M10x-P
(DCS – M10x – DCS) = 50ms
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions
Notes: Note 1: The line must be in Green theme

## Slide 25: Serial Communication: Modbus RTU Communication
Max 31 M10x-M devices per segment, max 57.6 kbps
Multiple segments not possible, bus termination needed
Typ. command execution time for one M10x-M
(DCS – M10x – DCS) = 50ms
MODBUS RTU
M10x-M No.1 M10x-M No. 2 M10x-M No. 3 …………. M10x-M No. 31
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions
Notes: Note 1: The line must be in Green theme

## Slide 26: Serial Communication: Modbus RTU Communication (redundant)
Max 31 M10x-M devices per segment, max 57.6kbps
Multiple segments not possible, bus termination needed
Typ. command execution time for one M10x-M (DCS – M10x – DCS) = 50ms
DCS controls redundancy, both M10x-M ports always active
2 x
MODBUS RTU
M10x-M No.1 M10x-M No. 2 M10x-M No. 3 …………. M10x-M No. 31
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions
Notes: Note 1: The line must be in Green theme

## Slide 27: Serial Communication: Other Protocols via Gateway
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions
Example: Moxa MB3170
Modbus RTU / TCP Gateway
Modbus TCP
Gateway solutions for Modbus TCP or PROFINET!
* Project applications are available.
Notes: Note 1: The line must be in Green theme

## Slide 28: Documentation Material LPLS & M10x Support Database
All Available in M10x Product Database!
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions

## Slide 29: Documentation Material M10x Product Documents
Marketing & Sales Documents *
Product Documents
& Other documents such as certificates and test reports etc.
* Also available in ABB library.
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions

## Slide 30: Documentation Material Demo Box
Complete M10x demo system
For presentation and testing purposes
Completely wired and fully equipped with M102-M & P, MD21, motor simulation
Ready to use
  Portable case
  Power supply 110 / 230 VAC for worldwide use
Contains
  M102-P and M102-M
  MD21 operator panel
  DI, DO simulation
  Motor simulation
  PC connection cable and MCUSetup software
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions
Notes: Photo 1: Photo shooting with angle and white background (refer to imagery_page14.pdf as per attached file)
Photo 2 & 3: Suggest to remove.

## Slide 31: Other ABB LV MCC solutions
ABB devices
UMC100
ABB Switchgear solutions
MNS iS
Introduction
Motor Management
Advantages of Intelligent Swgr
MNS3.0+M10x Solution
Project References
Product Guide
Serial Communication
Documentation Material
Other ABB LV MCC solutions
Notes: Note 1: