## Slide 1: Low Voltage Breakers and Switches Service Retrofitting kit 2014

## Slide 2
LCM
Retrofit Concepts
  The aim
  Benefits
  ABB retrofitting solutions for ACB
  ABB retrofitting solutions for MCCB
  ABB retrofitting solutions vs competitors
Scenarios
  Retrofill/ Direct Replacement/Cradle in Cradle
Certification
Driving factors
Manufacture Process
Special Solutions
Next Solutions
Maintenance Agenda

## Slide 3
Part and
inventory
management
Remote
condition
monitoring
Remote
Troubleshooting
Life cycle
assessment
1. Service Agreements
11.
Replacement
10. End of life
Services
9. Extension,
Upgrades
& Retrofit
8. Advanced
services
7. Engineering
& Consulting
6.
Repairs
5.
Maintenance
4. Spare &
Consumables
3.
Training
2. Installation &
commissioning
Installation
On-site
Training
Replacement
Parts
Preventive
maintenance
Engineering
planning and
specifications
Energy
Efficiency
Software
upgrades
Decommissioning
Replacement of
active products
Classroom
Training
Parts Kits
Predictive
maintenance
Data back-up
services
Programming
services
E-Learning
Consumables
On-site
condition
monitoring
Engineering
configuration
Extensions
Benchmarking
and audits
Retrofit
Replacement of
third party products
Extended
warranty
Technical
support
Inspections &
diagnostics
Refurbishment/
Reconditioning
services
Corrective
maintenance
Commissioning
On-site repairs
Hardware
upgrades
Replacement of
non active products
Workshop
repairs
Engineering
system
integration
ABB Low Voltage Breakers Service ABB Service portfolio

## Slide 4: ABB Low Voltage Breakers Service Replacement
Life Cycle Management – LCM
    ABB is a circuit breaker’s manufacturer, leader in Italy and even in the world, since 60’:
    ABB’s product lifecycle management model ensures predictable support of the life cycle and smooth transition to new technology.
    Customers are informed of the phase transition through ABB’s sales and service network.
Active
Classic
Limited
Obsolete

## Slide 5: ABB Low Voltage Breakers Service Replacement
Active  Normal production, sales and development phase
Classic  Product maintenance phase
Limited  Limited production and guaranteed availability of spares
Obsolete  Reduced availability of components and supports
ABB LPBS has divided the manufatured products into four phases
Mass Manufacturing End
Active
Classic
Limited
Obsolete
Guaranteed product support
Limited product support
approx 10 years
Lifecycle
announcement
Lifecycle
announcement
Product is released for sale
Annual lifecycle status review
Lifecycle
announcement
12 months
12 months
6 months
Last Buy

## Slide 6
© ABB Group
September 5, 2014 | Slide 6
ABB LPBS Life Cycle Management
Almost 50 years of products

## Slide 7: ABB Low Voltage Breakers Service Replacement
Substitute the complete System
Change the CB with an adapter kit  Retrofitting kit
Classic
Active
Limited
Obsolete
New CB +
Retrofitting kit
What can customer do?

## Slide 8: Retrofit Concept The aim
The retrofitting concept consists in the implementation of the new technology of circuit breakers on the existing switchboard:
  Cheaper than a new switchboard
  Shorter time for installation
  Minimum shutdown of the switchboard
  Circuit breaker’s life extension
  Improved Trip Unit protections
  Reducing of further maintenance costs
  Increasing of safety and reliability
  Spare parts availability for a longer time

## Slide 9: Retrofit Concepts Scenarios
Retrofill
The simplest solution where the existing fixed part is removed from the switchboard and the new one is installed using a pre-designed bus bar connection and protection shields.
Cradle in Cradle
La fixed part of the new CB is modified to be inserted in the old fixed part.
Direct Replacement
The moving part of the new CB has to be modified to simulate the moving part of the old CB. It requires a very short shutdown.
Notes: Replacement: Permette un fuori servizio brevissimo, ma richiede un pesante lavoro di progettazione e di modifica dell’apparecchio in quanto vanno riproposti tutti i blocchi, sistemi di inserzione, collegamenti di circuiti ausiliari etc etc. E anche la soluzione che richiede più prove di tipo e certificazione.

## Slide 10: ABB Low Voltage Breakers Service Retrofit solutions for ACBs
Otomax
LCM: Obsolete
Retrofitting kit (RF): Otomax-Emax
Cradle in Cradle (CiC) : Otomax-Emax
Novomax
LCM: Obsolete
Direct Replacement (DR): Novomax–Megamax
Retrofitting kit (RF): Novomax–Emax
Direct Replacement (DR): Novomax G30– X1
Megamax
LCM: Limited
Replacement: Megamax–Megamax
Retrofitting kit (RF): Megamax–Emax
Dreict Replacement: Megamax Emax (F1, F2 OD)
Emax (PR111/PR112/PR113)
LCM: Limited/Obsolete
Direct Replacement (DR): Emax–New Emax
Notes: Replacement: Permette un fuori servizio brevissimo, ma richiede un pesante lavoro di progettazione e di modifica dell’apparecchio in quanto vanno riproposti tutti i blocchi, sistemi di inserzione, collegamenti di circuiti ausiliari etc etc. E anche la soluzione che richiede più prove di tipo e certificazione.
10

## Slide 11: ABB Low Voltage Breakers Service Retrofit solutions for MCCBs
Isol/Fusol
LCM: Obsolete
Retrofitting kit (CiC): Isol-Isomax
Retrofitting kit (CiC): Fusol-Isomax
Modul
LCM: Obsolete
Retrofitting kit (DR): Modul–Isomax S7
Retrofitting kit (DR): Modul–Tmax T5, Tmax XT4, Tmax XT2
Limitor
LCM: Obsolete
Isomax
LCM: Classic
Replacement: Isomax–Isomax
Retrofitting kit (RF): S8-T8
Notes: Replacement: Permette un fuori servizio brevissimo, ma richiede un pesante lavoro di progettazione e di modifica dell’apparecchio in quanto vanno riproposti tutti i blocchi, sistemi di inserzione, collegamenti di circuiti ausiliari etc etc. E anche la soluzione che richiede più prove di tipo e certificazione.
11

## Slide 12: ABB Low Voltage Breakers Service Retrofit solutions vs Competitors
Terasaki
AT (ALH)
Retrofitting kit (RF): AT  New Emax
Schneider
Masterpact M
Retrofitting kit (RF): M32- M40  New Emax
H&W
HN/ LH
Retrofitting kit (RF): HN800…HN2000  New Emax
Retrofitting kit (RF): LH250…LH2000  New Emax
Notes: Replacement: Permette un fuori servizio brevissimo, ma richiede un pesante lavoro di progettazione e di modifica dell’apparecchio in quanto vanno riproposti tutti i blocchi, sistemi di inserzione, collegamenti di circuiti ausiliari etc etc. E anche la soluzione che richiede più prove di tipo e certificazione.
12

## Slide 13: Retrofill Otomax - Emax
Emax
Otomax

## Slide 14: Retrofill Otomax - Emax

## Slide 15: Retrofill Otomax - Emax
Retrofill Kit
Existing Busbar
Original busbars

## Slide 16: Direct Replacement Novomax G30 – Emax X1
Novomax G30
Emax X1

## Slide 17: Direct Replacement Novomax G30 – Emax X1
Jaw contacts
Heat Pipes
Insertion guide
Auxiliary circuits plugs
Lock in open position
New Operating mechanism
Trip Unit

## Slide 18: Direct Replacement Novomax G30 – Emax X1
Max rated voltage Ue | [V] | 660
Rated insulation voltage Ui | [V] | 1000
Rated impulse withstand voltage Uimp | [kV] | 12
Rated frequency | [Hz] | 50-60
Rated ultimate breaking capacity under short-circuit Icu | [kA] | 45 @450Vac 35 @ 660Vac
Rated short-time withstand current Icw | [kA 1s] | 35
Rated current | [A] | 1600

## Slide 19: Direct Replacement Novomax G30 – Emax X1

## Slide 20: Direct Replacement Modul – Tmax/ Tmax XT
Old fixed part
Matching plate
CB fixed
Conversion kit from fixed to moving part

## Slide 21: Cradle in Cradle Isol/ Fusol - Isomax
Fixed part of Isomax inside the old fixed part of Isol / Fusol
Retrofitting kit Isomax
Old CB Isol / Fusol Moving Part
Old CB Isol/Fusol Fixed Part

## Slide 22: Cradle in Cradle Otomax-New Emax

## Slide 23: Direct Replacement Megamax-New Emax

## Slide 24: Direct Replacement
Megamax
OPEN DOOR (OD)
CLOSE DOOR (CD)

## Slide 25: Direct Replacement Megamax-New Emax Open Door
Megamax/Novomax Draw out lever
New Emax spacial moving part preassembled in ABB
Megamax/Novomax Fixed part (already insalled in the Switchgear)
Insulating plate
Push botton to unlock the draw out mechanism
Adapter pre wired connecting devices
The kit consists in:
Special New Emax moving part
Standard Megamax/Novomax sliding contacts (left and right) and dedicated wiring
Draw out lever
Door flange
Coils support
Mechanical signalling of circuit breaker tripped
Anti-insertion locks
Lifting golfare

## Slide 26: Direct Replacement Megamax-New Emax Open Door

## Slide 27: Direct Replacement Megamax-New Emax Open Door

## Slide 28: Direct Replacement Megamax-New Emax Closed Door

## Slide 29: Certifications Type Test
All our retrofitting kits are certificated:
All kits are developed by the same technicians who developped the CB itself
All kits are tested in accordance to Standards IEC 60947-2

## Slide 30: Certifications Driving Factors
The driving factors for the design of a kit are the same of a new CB:
dielectric properties in normal service and in case of short circuit
thermal behaviour (rated current and short time)
short circuit current withstand
mechanical fit:
  easy to install, to reduce the customer “out of service” for replacement
  to consider the switchboard access (front or rear) for installation
  new vs old cb dimension, busbars compatibility
  auxiliary connections

## Slide 31: Manufacture Process Retrofitting kit customization / Routine and special test
Special test
Replacement/
Cradle in Cradle Assembling
Routine test
Customized Accessory options
Accessories wiring check
Schematic dgr. Check
Dimensional check
Interlock check
Vibration tests

## Slide 32: Retrofitting kits Next solutions (2014)
1. Direct Replacement Megamax/ – Emax
Megamax F1/F2 CD E2 (2000A)
Megamax F4/Novomax G4  E3 3200 (OD + CD)
2. Emax  Emax 2
3. S8T8

## Slide 33: Retrofitting kits Next solutions (during 2014-2015)
ABB vs Competitors
3WN (Siemens)