## Slide 1: LMT series magnetostrictive level transmitters
Global launch
LMT Series, 2019
Customer presentation
Sreekanth Madhavasherry Sreenivasan (Sree), Global Product Manager, Level Products

## Slide 2: Agenda
Introduction
Operating principle
Features & functionality
Configurations
Key applications
  Product portfolio
  Summary

## Slide 3: Introducing ABB’s LMT Series
Next generation magnetostrictive level transmitters

## Slide 4: Evolution of magnetostrictive level measurement
Level
Loop Current
Magnetostrictive
Reed Switch
(incremental output)
  Since Archimedes’ famous eureka moment in his bathtub, buoyancy and the principles which support it have been one of the most widely used in the process instrumentation world.
  Magnetostriction is a property of ferromagnetic materials that causes them to change their shape or dimensions during the process of magnetization. The variation of materials' magnetization due to the applied magnetic field changes the magnetostrictive strain. The effect was first identified in 1842 by James Joule.*
  Reed chain transmitters, widespread popularity in the instrumentation world, particularly for level measurements, around the 1960s
  ABB’s SPM Series(K-Trak) ** was one of the pioneers in adopting the magnetostrictive technology in early 90’s followed by the AccuTrak AT Series transmitters with patented sensor design.*
Once upon a time…

## Slide 5: The magnetostrictive technology is well established in the market…
  For more than 15 years, ABB’s magnetostrictive level transmitters have been the market leader due to their performance and durability in tough industrial applications.
  Magnetostrictive technology is the most accurate liquid level transmitter technology in the world today.
Interaction of magnetic fields causes a torsional wave.
Magnetic field encompasses entire transmitter wire
Spring
Transmitter
Probe
Interrogation
pulse
Moveable position magnet
Magnetic field from position magnet
Pickup

## Slide 6: …good becomes better with LMT Series
1st LMT in service since July 2015
Loaded with features, benefits
A new generation of magnetostrictive liquid level transmitters

## Slide 7: Introducing new LMT Series
AT Series
Advanced LMT Series
Classic Design with component obsolescence threat and limited features
New & improved features with all major hazardous location approvals
Transition

## Slide 8: Introducing the LMT Series
Next Generation Magnetostrictive Transmitter
The LMT’s principle of operation and simple setup ensure customer process is always measured reliably and accurately. This allows them to maximize their process efficiency, uptime and profits.
  LMT is available as an insertion style “wetted” transmitter (LMT100) or as an externally mounted, non-intrusive design (LMT200) for use with the market leading KM26 magnetic level gauge or with any other float and level chamber.
Why LMT Series?

## Slide 9: Magnetostrictive level measurement
Operating principle
  The device electronics generates a low energy current pulse at fixed intervals.
  The electrical pulses create a magnetic field which travels down a specialized wire inside the senor tube.
  The interaction of the magnetic field around the wire and the magnetic float causes a torsional stress wave to be induced in the wire. This torsion propagates along the wire at a known velocity, from the position of the magnetic float and toward both ends of the wire.
  A patented sensing element placed in the transmitter assembly converts the received mechanical torsion into an electrical return pulse.
  The microprocessor-based electronics measures the elapsed time between the start and return pulses (Time of Flight) and converts it into a position measurement which is proportional to the position(level) of the float.
  Technology
LMT100 - Direct insertion LMT200 - Gauge mounted

## Slide 10: Key features and functionalities
ABB’s LMT Series magnetostrictive level transmitters

## Slide 11: LMT Series magnetostrictive transmitters
Features & functionality
    Superior sensor design – patented AccuTrack Torsional Piezo Sensor
    Integrated interactive waveform
    Safety integrity level : SIL2 / SC3 ( SIL2 (HFT=0), SIL3(HFT=1) accord. IEC61508
        ABB common look and feel
        Modular and flexible design concept – housing and HMI display
        Mounting flexibility enabling late configuration
        High accuracy level measurement
        4-in-1 measurement : total level, interface, temperature & Ullage
        Advanced diagnostics and online self-verification
        Variable process connections
        Model differentiation – LMT100 direct insertion and LMT200 gauge mounted
Features

## Slide 12: LMT Series magnetostrictive transmitters
Features & functionality
    Approvals: ATEX, IECEx, FM US & Canadian, NEPSI, CRN, EAC & INMETRO
    4-20mA with HART 7 & Foundation Fieldbus ITK6.3, Profibus in progress ) -Built-in RFI/EMI filter
        Modular design enabling field replace/upgradable electronics
        Dual compartment housing with separate field terminal compartment and secondary seal
        Meets NAMUR recommendations NE43, NE107 & NE131
        Pressure to 165.48 bar (2400 psig) Std. 124.1 bar (1800 psig)
        Temperature range: -195.5 to 426.6ºC (-320 to 800ºF)
        Loop powered to 22m (75ft) probe length
        Digital communications with software tools – DTM, EDD, FDI
        Advanced semiconductor platform with faster update rate , built-in surge protection option
Features

## Slide 13: LMT Series magnetostrictive transmitters
Features & functionality
0.01% of full scale or 0.05”,whichever is greater
0.005% of full scale or 0.015”, whichever is greater
Up to 10 updates per second
Accuracy
Repeatability
Update Rate
Measurement signal quality is unaffected by process conditions
Reliability
Total level, Interface level, Process temperature
Measurements

## Slide 14: LMT Series magnetostrictive transmitters
Performs well with
higher temperatures and pressures
longer sensor length requirements
higher distances from the chamber
  Provides
  real continuous measurement compared to a step output of reed chain transmitters
  lower total cost of ownership
  accurate, reliable & repeatable measurement
Our sensor provides a maximum transfer of the torsional energy and self-cancellation of longitudinal vibration.
Superior Sensor (Patent #5,473,245)
Features & functionality

## Slide 15: LMT Series magnetostrictive transmitters
  Proven sensor design
  Patented piezo ceramic torsional wave sensor
  High temperature and vibration applications
  Proven and industry leader with more than 100,000 installations
  Integrated Interactive Waveform
  Easy for commissioning and/or troubleshooting
  Powerful features with advanced tools for best-in-industry asset optimization
  Threshold, blocking distance, signal polarity and pulse gain adjustments
  Adaptable and flexible design to meet any installation challenges
  Elbow design allowing late configuration in mounting orientation
  Rotatable housing and display
  Aluminum or SS dual compartment for increased safety
Features & functionality

## Slide 16: LMT Series magnetostrictive transmitters
  4-in-1 measurement technology
  Single device measures level, interface, temperature & ullage
  Most accurate technology for interface measurement
  Wide range of float selection depending on application – no batteries in the float
  Meeting NAMUR recommendations
  NE131 NAMUR Standard device- user roles and easy setup
  NE 43 NAMUR Standardization of the signal level
  NE 107 NAMUR Self-monitoring and diagnosis
  Digital communications
  DTM, EDDL, FDI and TTG Display - Flexible calibration and verification methods
  HART 7, Foundation Fieldbus ITK6.3 and Profibus* including 4..20mA analog output
Features & functionality

## Slide 17: LMT Series magnetostrictive transmitters
  Solution for every application
  Direct insertion vs gauge mounted- calibrated and assembled completely from factory
  Wide range probe options and process connection materials
  Works without display, dual compartment Aluminum or SS housing, built-in EMI filter
  Common platform across instrumentation
  Common TopWorks platform across instrumentation products
  Simplified operation, maintenance and training – a common user experience!
  First magnetostrictive transmitter with Through-The-Glass (TTG ) technology
  Faster measurement when every drop counts
  MCU and FPGA in the sensor board resulting in improved response time
  Improved measuring algorithms and detection techniques
  Advanced semiconductor platform with faster update rate , built-in surge protection option
Features & functionality

## Slide 18: LMT Series magnetostrictive transmitters
  Advanced on-line verification and diagnostics
  Sensor hardware check including internal connections check and sensor memory failure
  Internal electronics check including user configuration check and operating conditions
  Menu , EDD, FDI and DTM based verification
  Process Safety
  Secondary process seal for increased safety
  Glass to metal seal tested for more than 2000 psi pressure.
  All probes hydro tested to 1.5 times application pressure
  A higher level of measurement confidence
  Hazardous approvals – cFMus, ATEX/IECEx, NEPSI, CRN
  Safety integrity Level 2(SIL2) and Systematic Capability 3 (SC3 ) according to IEC61508
  Can be used in applications up to SIL2(HFT=0) resp. SIL3 (HFT=1)
Features & functionality

## Slide 19: LMT Series magnetostrictive transmitters
Features & functionality
Threshold(THD) in the waveform is the signal baseline
Signal peak shall cross the THD to have a valid measurement
THD can be adjusted to have the optimum performance throughout the range for the given application
Threshold(THD)
Blanking(BLK)
Blanking/blocking distance(BLK) is an useful feature to filter any noise near the start of the waveform.
Useful to have this value if noise introduced when level is near the device or due to any other inherent signal disturbances near the start of the signal
Pulse width(PLS)
Pulse width (PLS) increases/decreases the signal strength (gain).
Useful for asset optimization in case of the low magnetic strength in the float.
Optimize the PLS and/or THD value in longer probes for improved performance or in application with vibration
Signal polarity(SIG)
Inverts the signal polarity/the waveform
Useful when floats are installed incorrectly or he magnetic field orientation is reversed
Feature to reduce maintenance or risk of shutdown

## Slide 20: LMT Series magnetostrictive transmitters
Maintenance required
Out of specification
Check function
Failure
Sensor
Level Sensor Failure
Sensor Board Fault
Sensor Communication Failure
Temperature sensor failure
Electronics
Electronics Memory Failure
Electronics Insufficient Input Voltage
Operating and process conditions
Level Sensor Out of Limits
Temperature Sensor Out of Limits
Installation and start up
Data Simulation Warning
Sensor Configuration Warning
LMT Diagnostics per NE 107 include:
Features & functionality
Diagnostics
  NAMUR compliant
Built-in waveform
  Best asset optimization
Modular design
  Rotatable head and display
User experience
  Common platform

## Slide 21: LMT Series magnetostrictive transmitters
  Common Look and feel throughout ABB level and other instrumentation products
    Level –Ultrasonic, Laser
    Flow
    Pressure
    Temperature
    Positioner
    Analytics
    Recorders and Controllers
ABB common look and feel - within all ABB instrumentation products
Features & functionality

## Slide 22: LMT Series magnetostrictive transmitters
First magnetostrictive transmitter with TTG (Through The Glass) technology.
- Graphic display with four key operation
- Configuration in hazardous areas without powering off the transmitter
Easy to use in field
  HART 7 & FF ITK 6.3 communication with
    HHT 475
      Emerson AMS
        Emerson DeltaV & other systems
Integrated HMI
EDD in Handheld terminal
Device integration
Efficient intelligent device management
- Open, standardized interface
Support full device functionality
Seamless communication with various host control systems
DTM in Control Systems
ABB presents the world's first FDI supported device management tool FIM (Field Information Manager) - Seamless communication with various host control systems
- LMT FDI device packages
FDI device packages
Notes: Field Information Manager, the first FDI-based software for device management, makes the configuration, commissioning, diagnostics and maintenance of fieldbus instruments easier and quicker than ever before. Support full device functionality

## Slide 23: LMT Series magnetostrictive transmitters
Superior features, simpler to use, safe & reliable
Feature | Safety | Ease of Use | Flexibility | Reliability
Onboard Waveform Display & Diagnostics | ü | ü | ü | ü
Easy Setup Menu |  | ü |  | 
Dual Compartment with secondary Sealed Electronics | ü |  | ü | 
Floats do not require batteries | ü | ü | ü | ü
Reliable interface measurement | ü | ü | ü | ü
DTM & EDDs for Remote viewing and calibration |  | ü | ü | ü
Built-in RTD Option – LMT100 wetted sensor |  |  | ü | 
Mounting orientation can be changed in field |  | ü | ü | 
High Temperature & Cryogenic Capabilities |  |  | ü | ü
Non-Intrusive - Externally Mounted LMT200 | ü | ü | ü | ü
Insertion Well for removal even when process is in vessel | ü | ü | ü | 
HART 7 & FF ITK6.3 Communication |  | ü |  | 
ATEX/IECEx, cFMus, NEPSI, EAC, INMETRO, SIL2/3 | ü |  |  | ü

## Slide 24: Key configurations
ABB’s LMT Series magnetostrictive level transmitters

## Slide 25: LMT Series magnetostrictive transmitters
LMT100 and LMT200
LMT100: accurate level and interface measurement
LMT200: valve position transmitter
LMT200: non-intrusive configuration

## Slide 26: LMT Series magnetostrictive transmitters
LMT100
LMT100 with sensor well
5/8” Sensor Options - R1, R2, R3, C1, C2, H1, H2
½” Sensor Options – R4 and R5
Sensor Well Options – W1, W2, W4, W5, W6, C3, C4
Compression fitting
Level and Interface float
Flanged process connection
Configurations
Flanged and compression fitting process connection

## Slide 27: LMT Series magnetostrictive transmitters
LMT100 flexible sensor
LMT100 with jacketed sensor
Flexible sensor options – W3 and W7
PFA Jacketed Sensor Options – J1, J2, J4, J5
W7 – Segmented metal sensor well with flexible PFA sensor
W3 - Metal sensor well with flexible braided SS sensor
PFA jacked sensor and sensor well
Configurations

## Slide 28: LMT Series magnetostrictive transmitters
LMT200
LMT200 with 90o bend sensor
LMT standard mounted on MLG chamber
LMT 90o bend on MLG chamber
Flexible configurations
For cryogenic and extreme temperature applications
Configurations

## Slide 29: Key Applications
ABB’s LMT Series magnetostrictive level transmitters

## Slide 30: LMT Series magnetostrictive transmitters
Tough process conditions – Easy to apply, powerful results
Applications
Total level and Interface level
Interface with heavy emulsion layer
Extreme pressures and temperatures
Extremely low specific gravity
Extreme foaming
Steam and heavy vapors
Toxic vapors and fluids
Condensing atmospheric conditions
Hydrocarbons, acids or basic chemicals
Turbulent surfaces
Viscous fluids
Paraffin's and buildup can be defeated
Extreme accuracy requirements
LMT Series: Intrusive or nonintrusive level measurement

## Slide 31: LMT Series magnetostrictive transmitters
Power
Chemicals
Oil & gas
Pulp & paper
Water & wastewater
Boiler level
Feedwater heater level
Ammonia Vaporizer Control
Condensate tanks
  Sump level
  Purified Water Level
  Chemical storage tanks
  Floatation Cell Level
  Purified Water Level
  Chemical storage tanks
  Hydrocarbon Storage Level
  Separator HT/LT
  Distillation Column
  Propane storage
  Glycol
  Acid storage tanks
  Cryogenic
  Oleum Acid Tower
  HCL storage tanks
  Ion exchange tanks
Applications

## Slide 32: Portfolio
ABB’s LMT Series magnetostrictive level transmitters

## Slide 33: LMT Series magnetostrictive transmitters
Portfolio transition
AT Series |  | LMT Series | 
AT100 |  | LMT100 Direct insertion | 
AT200 |  | LMT200 Gauge mounted | 
AT500 |  | LMT100 Blank cover without Display | 
AT600 |  | LMT200 Blank cover without Display | 
Top performance at an attractive price level for a competitive Market!

## Slide 34: LMT Series magnetostrictive transmitters
Base
Standard
Premium
Top
  316SS Housing
  TTG display and all approvals
  Corrosive and offshore application
Standard
  Aluminum Housing
  TTG Display, all approvals
  Replaces AT100/200
Economy
  No Display, Blind Cover
  OEM Applications
  Replaces AT500/600
Features
Positioning – LMT100 and LMT200

## Slide 35: Summary
LMT Series – To help you do your level best

## Slide 36: LMT Series – benfits in a glance
Easy to apply, powerful results
Easy display view at any angle
Vertical head rotation
Easy calibration
Waveform Display
No oscilloscope required
Improved Diagnostics
NE107 Messaging
Troubleshooting assistance
Reliable performance with foam, emulsion, flashing, steamy, and changing process conditions
Signal quality not process dependent
Safe for use in critical applications
IEC61508 Certified SIL2/3 Capable
Reliable performance
Easy modifications in the field
Common design for all mounting orientations
Reduced startup delays
Installation flexibility
Faster commissioning
Factory calibrated to your application
Minimal skill set required
Wide range of probe and process connection materials
For any application
Total level, Interface , ullage and temperature
4-in-1 measurement
Digital
Full assembly and accessories installed(LMT200), tested and calibrated and shipped from factory results in lower cost of ownership
No piping modifications or process interruptions to add transmitters to a KM26 MLG results in lower cost of ownership
Improved design results in increased accuracy of level measurement increasing the energy efficiency and throughput.
Advanced built-in diagnostics tools – minimizes downtime , increase asset life and modular parts results in maximize productivity and profits
Increased safety – global Hazloc approvals, secondary seal and SIL capability for critical applications
Customer benefits
4-20mA, HART7 & FF ITK6.3
EDD –integrated with HHT475
FDT DTM
FDI device packages for FIM

## Slide 37: LMT Series
ABB’s next generation magnetostrictive level transmitters
Wide environmental conditions:
  RoHS 2.0
  ATEX/IECEx, cFMus, CRN, NEPSI
Advantages
IP 66
  4..20mA, HART, FF/PA
Digital communications
  DTM, EDD, FDI
-40°C to 85°C
Key features
  SIL2/3 capable
  4-in-1: total level, interface , ullage & temperature
  Retrofittable in any MLG
  Variety & flexible mounting options
  Advanced diagnostics
  Easy startup and low maintenance
  360o rotatable HMI & housing
  Integrated interactive waveform
  Wide range of applications: Oil & Gas, Petrochem, chemical, Power etc.
  Patented piezo sensor
Lower total cost of ownership
  Improved Delivery : modular &late configuration
  Global Market: Hazloc approvals with SIL 2/3 capability
  Common parts: Optimize operations, inventory management
Meet market expectations
Ease of installation, mounting and configuration
Ease of commissioning & troubleshooting
Advanced tools for best asset management-reduce total cost of ownership
Variants based on applications
  All variants with all approvals - base model without display option– direct insertion vs gauge mounted
  Aluminum vs SS dual compartment
  ABB Technical support & service personnel's
Gain creators
Pain relievers
Products &
services